## Slide 1: Projects Overview
¿Questions?

## Slide 2
Patrick Herke
June 28, 2021
Internship Presentation

## Slide 3: SPACER
Safety Topic: First Aid

## Slide 4: Intern Summary Slide
Name: Patrick Herke
School and Year in College: Junior at Louisiana State University
Major: Mechanical Engineering
Project Title: Technical Intern, Mechanical Engineering
Team/Department: Maintenance
Supervisor: Todd Stephens
Fun fact: I write normally with my right hand, but
What Did You Learn?
Key Findings Results
Impact on The Business
Troubleshooting & parts sourcing
Pumps (sealed and magdrive)
Pressure Vessel Code Calcs
Conversion of ~7,900 documents
PSD audit
Code Calcs for 3 Vessels
Accessible documentation
Easier Pump Troubleshooting

## Slide 5
Troubleshooting & parts sourcing
Pumps (sealed and magdrive)
Pressure Vessel Code Calcs
Document management
Plant layout & PSD types
What Did You Learn?
Key Findings Results
Impact on The Business
Material incomp-atibility with process
Pump failure summary report
Code Calcs for 3 Vessels
Conversion of ~7,900 documents
PSD audit
Cost savings on order of ~50k/year
Easier Pump Troubleshooting
Calculate remaining life & audit compliance
Accessible documentation
Better inventory management of PSDs
Name: Patrick Herke
School and Year in College: Junior at Louisiana State University
Major: Mechanical Engineering
Project Title: Technical Intern, Mechanical Engineering
Team/Department: Maintenance
Supervisor: Todd Stephens
Fun fact: I write normally with my right hand, but

## Slide 6
Safety
Safety Tailgates
  June XX – Sleep deprivation
  July 24 – First aid kit and medications
Weekly Safety Observations
  Observe work
  Evaluate safety
Figure 1

## Slide 7: Overview of Projects
Projects
Filter Press Troubleshooting (SF2710) (w/Avery)
Pressure Vessel Calculations (w/Avery)
Rupture Disk Audit
Specifications and Standards Overhaul
Bad Actor Pumps Evaluation (w/ Avery)
Vendor Visits
Miscellaneous
Notes: -list of major projects I worked on this summer

## Slide 8
Filter Press Troubleshooting (SF2710) (w/ Avery)

## Slide 9: Filter Press Troubleshooting (SF2710) (w/Avery)
Problem
Plates warping
  Leaking
  Bypassing filter
  High liquid content in cakes
  Replacing every 2-4 months
Figure 2
Figure 4
Figure 3
Notes: Warping results in leaks and high liquid content in the cakes left behind
$12,000
Cloths should be cleaned (using a high pressure wash using water OR a recirculating a particulate dissolving solution within the press) or replaced as soon as they start blinding.

## Slide 10: Filter Press Troubleshooting (SF2710) (w/Avery)
Potential Causes
Material incompatibilities
Insufficient cleaning schedule/procedures
Uneven Cake Buildup
Findings
Slurry is 3-5 wt% sodium hydroxide (caustic) in water
  Also contains 500ppm-1wt% toluene
  Polypropylene plates not resistant to toluene
Cloths changed when plates are changed
  Cleaned by scraping
Figure 5
Figure

## Slide 11: Filter Press Troubleshooting (SF2710) (w/Avery)
Solution
Communicating with supplier about different material possibilities
Suggest implementing new cleaning schedule/procedure
  Cleaning or replacing cloths upon blinding
Figure
Benefits
Reduce maintenance costs
  For 3 month average lifespan
    Same material: ~$144,000 every 3 years
    New material:
      30% glass filled nylon: ~$62,000 per set
      PVDF: ~$100,000 per set
Improve functionality

## Slide 12
Pressure Vessel Calculations (w/ Avery)

## Slide 13: Pressure Vessel Calculations (w/ Avery)
Problem
Audit finding: Some pressure vessels are missing code calculations
  Minimum Thickness
  Maximum Allowable Working Pressure (MAWP)
  Remaining Life Calculations
Solution
Verify which vessels are missing calculations (Avery)
Find Identifying Information for Vessels
  Nameplates
  U-1 forms
  Drawings
  Other datasheets
Figure
Notes: Joint Project
Remaining Vessels with sufficient information

## Slide 14: Pressure Vessel Calculations (w/ Avery)
Solution (continued)
Contact Manufacturers
  Get drawings and/or code calculations
Remaining Vessels
  Build out the vessels in Compress
  Perform code calculations
Figure
Figure : TPT-36
Figure : PS-256

## Slide 15: Pressure Vessel Calculations (w/ Avery)
Benefits
Figure : D-2450
Created required documentation
Enhanced Safety
Remaining life calculations
Figure

## Slide 16
Rupture Disk Audit

## Slide 17: Rupture Disk Audit
Problem
Poor inventory management
Inconsistent replacement frequency
Solution
Inventory Audit
    Photograph Each Label in Stores
    Enter Identifying Data and Quantity into Spreadsheet
Figure

## Slide 18: Rupture Disk Audit
Solution (continued)
Field Audit
    Photograph Each Rupture Disk out in the Field
    Enter Identifying Data and Quantity into Spreadsheet
Compare both Spreadsheets to Find Gaps
    Identified X# of gaps
    Verified inventory of X# of disks
    Identified labelling issues
      Disk nameplates
      Piping & Instrumentation Diagrams
Figure
Benefit
Up to date inventory
Limit downtime
Limit spills

## Slide 19
Specs and Standards Overhaul

## Slide 20: Specifications and Standards Overhaul
Problem
Current pdf format does not allow for easy editing
+1000% required to read some document tables
Figure
Figure
Notes: Word template uses mailmerge fields
Set up the Laserfiche workflow so that it would recursively search through all the subfolders of the folder I ran it on.
Or if I gave it a document only run that document (allows for testing)

## Slide 21: Specifications and Standards Overhaul
Solution
~900 documents
  Convert from pdf to word with Adobe Acrobat DC Action Wizard
  Created Laserfiche Workflows to:
    Extract text data using OCR
    Use RegEx to extract data from the text
    Assign extracted data to document metadata
Figure
Figure
Notes: Engineering Specifications, Engineering Standards, and Piping Specifications

## Slide 22: Specifications and Standards Overhaul
Solution (continued)
~7,000 documents
  Created word template
  Created Laserfiche Workflows to:
    Extract the metadata of the pdf in Laserfiche
    Fill out the template using the metadata
    Assign the document to it’s new location
Figure
Figure
Benefits
Easily update as guidance changes
More accessible documentation
Notes: Fluids Symbols and Gaskets & Valve Equals

## Slide 23
Bad Actor Pumps Evaluation (w/ Avery)

## Slide 24: Bad Actor Pumps Evaluation (w/ Avery)
Problem
Assigned 2 bad actor pumps
P-202A mechanically sealed centrifugal pump
P-335 magnetically driven centrifugal pump
Solution
Discussed mechanics of sealed and magdrive pumps
Examined failure reports
Discussed potential troubleshooting options

## Slide 25: Bad Actor Pumps Evaluation (w/ Avery)
Problem
Assigned 2 bad actor pumps
P-202A mechanically sealed centrifugal pump
P-335 magnetically driven centrifugal pump
Solution
Discussed mechanics of sealed and magdrive pumps
Examined failure reports
  P-335: solids, pump running dry
  P-202A: product build up, seal chamber overpressure

## Slide 26: Bad Actor Pumps Evaluation (w/ Avery)
Potential troubleshooting options or solutions
  P-335: identify solid & source, recirculation line, filter pot
  P-202A: process chemistry, wash, tattletale
Solution (continued)
Revisit problem
Learning opportunity
Benefits
Figure

## Slide 27: Bad Actor Pumps Evaluation (w/ Avery)
Problem
Failure reports not combined anywhere
Big picture is hard to see
Solution
Created Summary of Failure Reports
  Uses Laserfiche forms
  Can adjust filters to select specific equipment
  Can automate generation
Benefit
Easier to troubleshoot
Big picture is clearer

## Slide 28
Vendor Visits

## Slide 29: Vendor Visits
AWC PSV Valve Shop Tour
Demonstration of inventory management software
Tour of shop and inventory
Explanation of valve testing bench
Instrument and controls training area
Firewater Pump
Potential reasons for failure
Inspection of pump components
Approval of repairs and changes
Figure
Figure
Figure
Notes: PSV valve shop
And manual and CV?
Which other?

## Slide 30
Miscellaneous

## Slide 31: Miscellaneous
MDUN meetings
Maintenance meetings
Cover ongoing projects
Discuss new issues
Flowserve meetings
Reliability metrics
Pump and seal failures for month
Potential long term solutions
BJFA Training
Helped evaluate presentation and quiz
Attended training
Figure
Figure

## Slide 32
Butterfly Garden Enhancement
Pulled weeds and transplanted plants
Analytical Labs Tour
NMR, ICP, DSC, Titration
Wildlife Habitat Tour
Documented wildlife
Importance
  Increases biodiversity
  Supports conservation
  WHC silver certification
  Corporate adoption
Figure
Figure

## Slide 33
Closing

## Slide 34: Closing
Acknowledgements
Nicole Stein
Daniel Dragland
Todd Stephens
Joe Haley
Bob Gallant
Debbie Meyer
Angelle Forrest
Tommy Ray
Catherine Morejon-Garcia
Jeremy Quirk
Lakeisha Butler
Gaya Elpitiya
Terry Temple
Jonathon